## Slide 1: Remote Sensing
For any given material, the amount of photon radiation that is reflected (absorbed, transmitted) will vary with wavelength.
Remote Sensing
Notes: <number>

## Slide 2: Thus, at some wavelengths, sand may reflect more light than green vegetation but at other wavelengths it absorbs more light (thus, reduced reflection) than does the now more reflective vegetation.
Notes: <number>

## Slide 3: Various kinds of surface materials can be recognized and distinguished from each other by these differences in relative reflectances
(GL = grasslands; PW = pinewoods; RS = red sand; SW = silty water)
Notes: <number>

## Slide 4: The task of any remote sensing system is simply to detect radiation signals, determine their spectral character, derive appropriate signatures, and interrelate the spatial positions of the classes they represent
Notes: <number>

## Slide 5: (Multi-Spectral Scanner) that has operated on all Landsat spacecraft
Light is gathered through a ground-pointing telescope
Light through each filter reaches its set of six electronic detectors
The continuous stream of pixel values can be used to drive an electronic device that generates a uninterrupted light beam of varying intensity which sweeps systematically over film
Notes: <number>

## Slide 6: MSS Band 4 = Blue MSSBand 5 = Green MSS Band 7 = Red
These two urban regions, along with Trenton on the Delaware River and the New Jersey cities along the Hudson appear in light to medium gray tones in Band 5 (red).
The color composite extends the coverage to include the northern Delmarva Peninsula flanked by the northern Chesapeake Bay (left) and Delaware Bay (center) and Cape May.
In Band 7 (IR), the central areas of these metropolitan complexes are rendered in dark tones, owing largely to the prevalence of asphalt streets and dark (usually asphalt) roofs together with low concentrations of trees and other vegetation,
Notes: <number>

## Slide 7
Notes: <number>

## Slide 8: Thematic Mappers
Band No. Wavelength Interval (µm)Spectral Response Resolution
(m)1 0.45 - 0.52 Blue-Green
2 0.52 - 0.60 Green
3 0.63 - 0.69 Red
4 0.76 - 0.90 Near IR
5 1.55 - 1.75 Mid-IR
6 10.40 - 12.50 Thermal IR
7 2.08 - 2.35 Mid-IR30
The six reflectance bands obtain their effective resolution at a nominal orbital altitude of 705 km (437 miles)
Notes: <number>

## Slide 9: Usages of band widths
Band 1 is superior to MSS 4 in detecting some features in water;
Band 5 is sensitive to variations in water content, both in leafy vegetation and as soil moisture;
Band 6 can distinguish a radiant temperature difference of ~ 0.6 degrees C and is helpful in discriminating rock types
Band 7 reacts to moisture contents and is especially suited to detecting clays
Notes: <number>

## Slide 10: TM Band 4 = red TM Band 3 = green TM Band 2 = blue Two color patterns dominate the land classes: reds, depicting vegetation, and medium grayish-browns, found mainly along the bright sun-facing slopes
The continuous and rather deep red at g represents a segment of the forested areas in the Los Padres National Forest near the crest of the Santa Lucia Mtns.
Elsewhere, as at i, thin strings of red or irregular red patches (j) can be largely attributed to trees and/or scrub vegetation (l) lining stream channels or scattered as copses and patches along the hillslopes.
In the valleys bright red areas, some rectangular and others more uneven, at k and other points are primarily examples of field crops, hay meadows, or other types of cultivation.
Areas believed to be barren to varying degrees, as at m and o, have darker gray-brown tones but may have faint pink overtones implying limited vegetation cover.
Notes: <number>

## Slide 11: The urban areas once again can be delineated largely from the street patterns. The streets, as well has Highway 1 and other major roadways, have bluish tones, expected because they are especially light-toned in bands 1 and 2 (assigned here to blue).
Areas postulated to support more actively growing grass, as at v, have a definite red-orange tone.
The vegetation within the coastal marsh (o) takes on a distinctive orange undertone, insinuating that some of the plants have a reddish coloration (remember, orange can result from a higher input of green-filtered light [assigned to the red band in making the composite] ).
The mystery area s just next to the marsh, and shown enlarged to the left, has a bright red expression alluding to the presence of highly IR-reflective vegetation such as might be found where grasses are luxurious
Notes: <number>

## Slide 12: Unsupervised Classification
the objective is to group multiband spectral response patterns into clusters that are statistically separable.
a small range of digital numbers (DNs) for, say 3 bands, can fix one cluster that is set apart from a specified range combination for another cluster (and so forth).
These can be modified so that the total number of clusters can vary arbitrarily. We picked 10
These levels can then be assigned colors to produce a cluster "map".
Notes: <number>

## Slide 13: The trick then becomes one of trying to relate the different clusters to meaningful ground categories.
The trick then becomes one of trying to relate the different clusters to meaningful ground categories.
This must be done by either being adequately familiar with the major classes expected in the scene under study or, where feasible, by visiting the scene itself - ground truthing
Notes: <number>

## Slide 14
Notes: <number>

## Slide 15
Notes: <number>

## Slide 16: Signature Graphs
BAND: 1 2 3 4 5 6 (TH)7 No. of Pixels
Seawater57.4 16.0 12.0 5.6 3.4 12.0 1.52 4332.
Sediments162.2 19.6 13.5 5.6 3.51 12.2 1.6 681
Notes: <number>

## Slide 17: Reduced Cluster Classifications will group usages
Notes: <number>

## Slide 18: More specific Classifications
Notes: <number>